Experiment no : 06

Aim: 			Design of Astable multivibrator for required frequency and Duty cycle using 			IC 555.

a) Duty cycle = 75 % and f = 1KHz

b) Duty cycle = 50% and f = 1 KHz

Apparatus: 		Op-amp IC 555, Breadboard, capacitor , CRO, CRO probes, resistors,

Function Generator, Dual power supply(0 – 30 V) , connecting wires , diode, 			potentiometer (10K) etc.

Circuit Diagram:

Theory:		The 555 timer is an integrated circuit (chip) implementing a variety of 				timer and multivibrator applications. The 555 gets its name from the three 5-			KΩ resistors used in typical early implementations.The timer basically 				operates in one of the two modes monostable (one-shot) multivibrator or as 			an astable (free-running) multivibrator. In the monostable mode, it can 				produce accurate time delays from microseconds to hours. In the astable 				mode, it can produce rectangular waves with a variable duty cycle.

The astable multivibrator generates a square wave, the period of which is 				determined by the circuit external to IC 555. The astable multivibrator does 			not require any external trigger to change the state of the output. Hence the 			name free running oscillator. The time during which the output is either high 			or low is determined by the two resistors and a capacitor which are externally 			connected to the 555 timer.

The above figure 1 shows the 555 timer connected as an astable 				multivibrator.  If the output is high initially, capacitor C starts charging 				towards Vcc  through R1 and R2.  As soon as the voltage across the capacitor 			becomes equal to 2/3 Vcc the upper comparator triggers the flip-flop, and the 			output becomes low. The capacitor now starts discharging through R2 and 			transistor Q1 . When the voltage across the capacitor becomes 1/3 Vcc the 			output of the lower comparator triggers the flip-flop, and the output becomes 			high. The cycle then repeats.

The capacitor is periodically charged and discharged between 2/3 Vcc and1/3 			Vcc respectively as shown in fig 3. The time during which the capacitor 				charges from 1/3 Vcc 	to 2/3 Vcc is equal to the time the output remains high 			and is given by

tON = tC = 0.693 ( R1 + R2 )*C

Similarly the time during which the capacitor discharges from 2/3 Vcc to 1/3 			Vcc is equal to the time the output is low and is given by

toff = td = 0.693 ( R2 )*C

Thus the total time period of the output waveform is

T = tON + toff = 0.693 ( R1 + 2 R2 )*C

Therefore the frequency of oscillation  :

f = 1/ T = 1.45 / ( R1 + 2 R2 )*C

The output frequency, f is independent of the supply voltage Vcc.

The Duty cycle is the ratio of the time tON for which the output is high to the 				time period T. It is generally expressed as a percentage.

% Duty cycle (D)  =  ( tON / T ) * 100

= [ ( R1 + R2) / ( R1 + 2R2) ]*100

According to the above relation, a duty cycle of less than 50% cannot be 				achieved. Also, 50% duty cycle, which corresponds to a square wave, can be 			achieved only if R1= 0 resulting in terminal 7 being directly connected to 			Vcc. When the capacitor discharges through R2 and  Q1 an extra current is 			supplied to Q1 by Vcc through the terminal 7 (now directly connected to 				Vcc ), which may damage Q1 and hence the timer.

Το obtain 50% duty cycle a diode should be connected across R1 and R1 			must be a combination of a fixed resistor ( usually 100 Ω) and a 				potentiometer. So that the pot can be adjusted for the exact 					square waves.

An alternative approach to achieve a duty cycle of less than or equal to 50% 			is to connect a diode D across resistor R2 as shown in Figure 2. In this case, 			the capacitor C charges through R1 and diode D to approximately 2/3 Vcc  			and discharges through R2 and transistor Q1 until the capacitor voltage equals 			approximately 1/3 Vcc, after which the cycle repeats.

Now the time for which the output is high is given by

tON = tC = 0.693 ( R1 )*C

Thus the total period of the output waveform is

T = tON + toff = 0.693 ( R1 + R2 )*C

Thus Duty cycle is % D = ( R1 / ( R1 +R2) ) *100

If R1= R2 , the duty cycle is 50% . For R1 < R2 , the duty cycle is less than 			 50%.

Calculations: 	Design of Astable Mutivibrator for 75% duty cycle and  f = 1kHz

Duty cycle: 	 D = [ ( R1 + R2) / ( R1 + 2R2) ] = 0.75

Solving we get , 	R1 = 2R2          ; Let C = 0.1 μF

T = 1ms , tOff  = 0.25ms = 0.693 ( R2 )*C

Thus , R2 = 3.6 KΩ  and  R1 = 7.2KΩ

Similarly, for Design of 50% duty cycle and 1KHz frequency

Let R1=R2 and C = 0.1 μF , follow the steps given in theory.

Procedure:      	1. Wire the designed circuit as shown in fig 1 with the calculated values of 			R1 , R2 and C for 75% duty cycle on the bread board.

2. Now connect one probe between pin 3 and pin 1 to see the (rectangular)			output waveform and connect the other channel of the CRO between pin 6 			and pin 1 to obtain the voltage across the capacitor.

3.  Measure the charging time tC and discharging time td and verify the 				observed frequency and duty cycle with calculated values.

4. Plot the waveforms observed of output voltage and the voltage across the 			 capacitor.

5. Repeat the steps (2) to (4) for 50% duty cycle , also connect a diode D 				across R2 and record the observations.

Observation table :

Table 1 : Duty cycle = 75% , f= 1 KHz, R1 = 7.2 KΩ, R2= 3.6 KΩ, C = 0.1 μF

| Parameters | Charging time tC or tON (sec) | Discharging time td or tOFF (sec) | Time period T (sec) | Frequency f (Hz) | Duty Cycle D (%) |
| --- | --- | --- | --- | --- | --- |
| Calculated | 0.75ms | 0.25ms | 1ms | 1KHz | 75 % |
| Observed |  |  |  |  |  |

Table 2 : Duty cycle = 50% , f= 1 KHz, R1 =R2, C = 0.1 μF

| Parameters | Charging time tC or tON (sec) | Discharging time td or tOFF (sec) | Time period T (sec) | Frequency f (Hz) | Duty Cycle D (%) |
| --- | --- | --- | --- | --- | --- |
| Calculated | 0.5ms | 0.5ms | 1ms | 1KHz | 50 % |
| Observed |  |  |  |  |  |

Results: 		An astable multivibrator of given duty cycle and frequency is designed. A 			comparison of the experimental values with the given ones is represented 			below:

| Quantity measured | Theoretical value | Experimental value |
| --- | --- | --- |
| Frequency |  |  |
| Duty Cycle |  |  |

# Text boxes

Pinout of IC 555

Fig 1 Astable Mutivibrator using 555 IC

Fig 2 Astable Mutivibrator using 555 for 50% Duty Cycle

Fig 3 Output and Capacitor voltage waveforms