Experiment no : 01

Aim: 			i)  Design  of Voltage Follower, Inverting and Non inverting

amplifier using Op-amp IC 741 and and test its performance.

ii) Design and implementation of linear equation for op- amp using IC 741.

1. VO = 3V1 + 5V2 – V3

2. VO  = 3V1 – 8V2

Apparatus: 		Op-amp IC 741, Breadboard,  multimeter, CRO, CRO probes, resistors,

Function Generator, Dual power supply(0 – 30 V) , connecting wires , etc.

Circuit Diagram:	Pinout of IC 741

1. Voltage Follower

Design: Vin = Vout [Unity Gain] & Rin = ∞ & Rf = 0

2. Inverting amplifier

Design: ACL = Vo/Vin = - Rf / Rin; Assume Rin = ______; Gain = _______;

3. Non inverting amplifier

Design: ACL= Vo/ Vin= 1 + Rf / Rin; Assume Rin = ______; Gain = _______;

4. Circuits for implementation of Linear equation using op-amp

Theory:		An operational amplifier or op-amp is a linear integrated circuit that has a

very high voltage gain, high input impedance and low output impedance.

Op-amp is basically a differential amplifier whose basic function is to 				 amplify the difference between two input signals.

Op-amp has five basic terminals, that is, two input terminals, one o/p terminal

and two power supply terminals. Pin2 is called the inverting input terminal

and it gives opposite polarity at the output if a signal is applied to it. It

produces a phase shift of 180o between input and output. Pin3 is called the

non-inverting terminal that amplifies the input signal without inversion, i.e.,

there is no phase shift or i/p is in phase with o/p. The op-amp usually

amplifies the difference between the voltages applied to its two input				 terminals. Two further terminals pins 7 and 4 are provided for the connection			 of positive and negative power supply voltages respectively. Terminals 1 and

5 are used for dc offset. The pin 8 marked NC indicates ‘No Connection’.

Op-amps have two operating configurations; open loop and closed loop. In

open loop configuration, it can operate as a switch but gain is uncontrolled.

In closed loop configuration, gain can controlled by feed back resistance Rf			 and input resistance Rin.

Procedure:      	1. Connect the components as per the circuit diagrams and wire them on

breadboard .

2.Connect dual power supply with (+15V) - 0 - (-15V) to the circuits with 			proper connections.

3. Set the input voltage 1V p-p / 1KHz using Function Generator  for circuits

(1-3)  and observe the output waveforms at Pin no.6 using CRO.

4. While designing the circuit for linear equations , measure the input 				voltages V1 , V2 , V3  etc and measure the output voltage VO  with a 				multimeter. Verify your design with calculated and observed results.

Observation table :

Op-amp as Voltage follower :

| Sr.no | Input Voltages Vin (volts) | Output Voltage Vo (volts) |
| --- | --- | --- |
| 1. |  |  |
| 2. |  |  |

Op-amp as Inverting Amplifier :

| Sr.no | Input Voltages Vin (volts) | Output Voltage Vo (volts) | Gain = - Rf / Rin |
| --- | --- | --- | --- |
| 1. |  |  |  |
| 2. |  |  |  |

Op-amp as Non-Inverting Amplifier :

| Sr.no | Input Voltages Vin (volts) | Output Voltage Vo (volts) | Gain = 1 + Rf / Rin |
| --- | --- | --- | --- |
| 1. |  |  |  |
| 2. |  |  |  |

Design of Linear Equation VO = 3V1 + 5V2 – V3 using op-amp

| Sr.no | Input Voltages | Output Voltage |
| --- | --- | --- |
|  | V1 | V2 | V3 | Vo |
| 1. |  |  |  |  |
| 2. |  |  |  |  |

Design of Linear Equation VO = 3V1 - 8V2  using op-amp

| Sr.no | Input Voltages | Output Voltage |
| --- | --- | --- |
|  | V1 | V2 | Vo |
| 1. |  |  |  |
| 2. |  |  |  |

Results: