Experiment no : 10

Aim: 			Design of R/2R ladder 4-bit D/A Converter using IC 741

Apparatus: 		Op-amp IC 741, Breadboard, Dual power supply(0 – 30 V) , connecting 				wires , etc.

Circuit Diagram:

R-2R ladder DAC using Opamp IC 741

Theory:			Real world signals are analogue. Digital systems that interface with 			the real world do so using analogue-to-digital converters (ADC). Conversion 			back to analogue is accomplished using digital-to- analogue converters 				(DAC). The R-2R ladder network is commonly used for Digital to Analogue 			conversions.

In basic N bit R-2R resistor ladder network the digital inputs or bits range 			from the most significant bit (MSB) to the least significant bit (LSB). The bits 			are switched between either 0V or VR and depending on the state and 				location of the bits Vo will vary between 0V and VR . The MSB causes the 			greatest change in output voltage and the LSB causes the smallest.

The R-2R ladder is inexpensive and relatively easy to manufacture since only 			two resistor values are required. It is fast and has fixed output impedance R.

In R-2R ladder type D to A converter, only two values of resistor is used (i.e. 			R and 2R). Hence it is suitable for integrated circuit fabrication. The typical 			values of R are from 2.5KΩ to 10KΩ . In this output voltage is a weighted 			sum of digital inputs. Since the resistive ladder is a linear network, the 				principle of super position can be used to find the total analog output voltage 			for a particular digital input by adding the output voltages caused by the 				individual digital inputs.The output voltage is linearly proportional to the 				digital input and the range can be adjusted by changing the reference voltage 			VR .

Calculations:		Output Voltage is given by

Vo = - VR * (Rf / 2R) * ( d1/2 + d2/4 + d3/8 + d4/16)

where, VR = 5V , Rf = 2R , d1 (MSB bit ) and d4 (LSB bit )

Let R = 12KΩ , then

Resolution = VFS / ( 2n- 1 ) , where n= no of  digital inputs

VFS = Value of analog output when digital input is 1111.

Resolution = 0.3125 = Value of LSB bit.

Procedure:      	1. Wire the  R/2R ladder 4 bit DAC circuit on the bread board.

2. Select the approximate value of R and 2R.

3. Reference voltage VR is set as 5V .

4. Find the output voltage Vo for different combinations of digital binary 				inputs from 0000 to 1111.

5. Compare the calculated values with observed values and plot DAC 				characteristics.

Observation table :

| d1 | d2 | d3 | d4 | Vo ( observed) | Vo ( Calculated) |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |  |  |
| 0 | 0 | 0 | 1 |  |  |
| 0 | 0 | 1 | 0 |  |  |
| 0 | 0 | 1 | 1 |  |  |
| 0 | 1 | 0 | 0 |  |  |
| 0 | 1 | 0 | 1 |  |  |
| 0 | 1 | 1 | 0 |  |  |
| 1 | 1 | 1 | 1 |  |  |
| 1 | 0 | 0 | 0 |  |  |
| 1 | 0 | 0 | 1 |  |  |
| 1 | 0 | 1 | 0 |  |  |
| 1 | 0 | 1 | 1 |  |  |
| 1 | 1 | 0 | 0 |  |  |
| 1 | 1 | 0 | 1 |  |  |
| 1 | 1 | 1 | 0 |  |  |
| 1 | 1 | 1 | 1 |  |  |

Result :